## Slide 1: Robot Car 2 (Wireless Communication Control) (RCC)
(Lesson Ref: RCC02)
RCC02: NRF24L01 Wireless Setup Tx-Rx

## Slide 2: Robot Car2 - Contents
Car 2 Transmitter Module (Front)
Car 2 Transmitter Module (Back)
Bluetooth Connector
Free Connector
Colour Sensor Connector
Gesture Sensor Connector
NRF 24L01
Transmitter
Joystick
Accelerometer
OLED
Mode
Button
Mini
Breadboard
Arduino
Uno
18650 Battery Holder
Button Control

## Slide 3: Robot Car2 - Contents
Car 2 Receiver Module (Front)
Car 2 Receiver Module (Back)
Car2 Receiver Motor Controller Board
NRF 24L01
Receiver
OLED
TB6612 Motor Driver
Battery Connector
18650 Battery Holder
Castor Wheel
DC Motors

## Slide 4: RCC02: NRF24L01 Wireless Setup TxRx
Things Needed
Car 2 Receiver Module
Car 2 Transmitter Module

## Slide 5: RCC02: Joystick Basics
Read X & Y values
Determine direction
Clear OLED & print
Small delay
Code for Lesson RCC02 (RCC02_a_Joystick_Movement_Functionality_Tx.ino):
Car 2 Transmitter Module

## Slide 6: RCC02: Joystick Basics
setup() • Start Serial (9600) for debugging • Initialize OLED display (SSD1306) at I2C address 0x3C • Clear display, set text size and color (WHITE) • Set joystick pins A0 (X) and A1 (Y) as INPUT
loop() • Read joystick analog values: xValue = analogRead(A0), yValue = analogRead(A1) • Convert X/Y values into a direction using thresholds: - Y > 600 → FORWARD - Y < 400 → BACKWARD - X > 600 → RIGHT - X < 400 → LEFT - Otherwise → CENTER • Clear OLED and set cursor to top-left • Display heading “JOYSTICK VALUES” • Print X, Y, and DIR (direction text) • Push updated frame to OLED using display.display() • Delay 50 ms for smooth refresh
directionText(x, y) • Checks joystick X/Y against fixed thresholds • Returns one of: FORWARD / BACKWARD / LEFT / RIGHT / CENTER

## Slide 7: RCC02: NRF24L01 Wireless Setup TxRx
Code for Lesson RCC02 (RCC02_b_NRF24L01_Basic_Transmitter_Tx.ino):
Code for Lesson RCC02 (RCC02_b_NRF24L01_Basic_Receiver_Rx.ino):

## Slide 8: RCC02: NRF24L01 Wireless Setup TxRx
Note:
Ensure both the receiver/transmitter have the identical Device Address (Pipe) and Channel
setup() • Start Serial (9600) • Init OLED (SSD1306, I2C 0x3C) • Init nRF24L01 as receiver – CE=A3, CSN=A2 – Reading pipe "00001" – Channel 108, Power LOW – startListening()
loop() • Show RECEIVER on OLED • If radio data available: – Read x, y payload – Display X and Y values • Refresh OLED • Delay 100 ms
setup() • Start Serial (9600) • Init OLED (SSD1306, 0x3C) • Init nRF24L01 as TX – CE=A3, CSN=A2 – Pipe "00001",
- Channel 108, Power LOW – stopListening() • Set joystick pins A0, A1 as INPUT
loop() • Read joystick X, Y • Send payload via radio.write() • Display TRANSMITTER, X, Y on OLED • Delay 100 ms

## Slide 9: Applications
Remote robot control
Telemetry monitoring
Multi-node communication

## Slide 10: Q&A
Why matching pipes?
Why CE/CSN?
Why OLED for debugging?