## Slide 1: Robot Car 2 (Wireless Communication Control) (RCC)
(Lesson Ref: RCC03)
RCC03: Robot Car Control Using Joystick

## Slide 2: Robot Car2 - Contents
Car 2 Transmitter Module (Front)
Car 2 Transmitter Module (Back)
Bluetooth Connector
Free Connector
Colour Sensor Connector
Gesture Sensor Connector
NRF 24L01
Transmitter
Joystick
Accelerometer
OLED
Mode
Button
Mini
Breadboard
Arduino
Uno
18650 Battery Holder
Button Control

## Slide 3: Robot Car2 - Contents
Car 2 Receiver Module (Front)
Car 2 Receiver Module (Back)
Car2 Receiver Motor Controller Board
NRF 24L01
Receiver
OLED
TB6612 Motor Driver
Battery Connector
18650 Battery Holder
Castor Wheel
DC Motors

## Slide 4: RCC03: Robot Car Control Using Joystick
Things Needed
Car 2 Receiver Module
Car 2 Transmitter Module

## Slide 5: RCC03: Robot Car Control Using Joystick
Code for Lesson RCC03 (RCC03_Robot_Car_Joystick_Control_Tx.ino):
Code for Lesson RCC03 (RCC03_Robot_Car_Joystick_Control_Rx.ino):

## Slide 6: RCC03: Robot Car Control Using Joystick
Compact Code Summary
setup() • Start Serial (9600) • Init OLED (SSD1306, 0x3C) • Init nRF24L01 as TRANSMITTER (CE=A3, CSN=A2, addr "00001", ch 108, pwr LOW) • Set joystick pins A0 (X), A1 (Y) as INPUT
loop() • Read joystick X, Y • Send {x, y} payload via nRF24L01 • Display TRANSMITTER, X and Y on OLED • Delay 100 ms
Compact Code Summary
setup() • Start Serial (9600) • Init motor pins and set fixed PWM speed (150) • Init OLED (SSD1306, 0x3C) • Init nRF24L01 as RECEIVER (CE=A3, CSN=A2, pipe "00001", ch 108, pwr LOW)
loop() • Display CAR RECEIVER on OLED • If radio data available: – Read joystick X, Y – Decide motion: FORWARD / BACKWARD / LEFT / RIGHT / STOP – Drive motors accordingly – Display X, Y and direction • Refresh OLED, delay 100 ms
Note:
Ensure both the receiver/transmitter have the identical Device Address (Pipe) and Channel