## Slide 1: Robot Car 2 (Wireless Communication Control) (RCC)
(Lesson Ref: RCC06)
RCC06:Robot Car Control Using Mode Button

## Slide 2: Robot Car2 - Contents
Car 2 Transmitter Module (Front)
Car 2 Transmitter Module (Back)
Bluetooth Connector
Free Connector
Colour Sensor Connector
Gesture Sensor Connector
NRF 24L01
Transmitter
Joystick
Accelerometer
OLED
Mode
Button
Mini
Breadboard
Arduino
Uno
18650 Battery Holder
Button Control

## Slide 3: Robot Car2 - Contents
Car 2 Receiver Module (Front)
Car 2 Receiver Module (Back)
Car2 Receiver Motor Controller Board
NRF 24L01
Receiver
OLED
TB6612 Motor Driver
Battery Connector
18650 Battery Holder
Castor Wheel
DC Motors

## Slide 4: RCC06:Robot Car Control Using Mode Button
Things Needed
Car 2 Receiver Module
Car 2 Transmitter Module

## Slide 5: RCC06:Robot Car Control Using Mode Button
Code for Lesson RCC06 (RCC06_Mode_Selection_Using_Mode_Button_Tx.ino):
Code for Lesson RCC06 (RCC06_Mode_Selection_Using_Mode_Button_Rx.ino):

## Slide 6: RCC06:Robot Car Control Using Mode Button
RCC06_Mode_Selection_Using_Mode_Button_Tx.ino
RCC06_Mode_Selection_Using_Mode_Button_Rx.ino
setup()
Init I2C, OLED display (SSD1306, 128×64, addr 0x3C)
Init MPU6050 accelerometer and calibrate gyro offsets
Init NRF24L01 as TRANSMITTER (CE=A3, CSN=A2, pipe=0xE8E8F0F0E1, PA=LOW)
Configure push buttons (UP, DOWN, LEFT, RIGHT)
Configure mode-select button and status LED
Display initial Mode and Status on OLED
loop()
Check mode-select button to cycle control modes
Select control logic based on current mode:
  Mode 0 → Button control
  Mode 1 → MPU6050 tilt control
  Mode 2 → Joystick control
Send direction commands wirelessly via NRF24L01
Update OLED with current Mode and Status
setup()
Init Serial communication
Init OLED display (SSD1306, 128×64, I2C, addr 0x3C)
Display startup message on OLED
Configure motor control pins (IN1–IN4, ENA, ENB)
Stop motors at startup
Init NRF24L01 as RECEIVER
  CE=A3, CSN=A2, pipe=0xE8E8F0F0E1
  PA level = LOW, Listening mode enabled
loop()
Check for incoming NRF24L01 data
Read command string from transmitter
Normalize command text (lowercase)
Decode command and map to motion:
  up → Forward
  down → Backward
  left → Left
  right → Right
  otherwise → Stop
Drive motors using PWM speed control