## Slide 1: ZAS Robotic Products
Navigational Robotic Series
Robot Car-2: Communications
Lab Session 7 – Bluetooth Control

## Slide 2: Lab Session 7 – Bluetooth Control
HC-05/HC-06 Bluetooth module
Phone → Car control
Serial command protocol
OLED debugging

## Slide 3: Learning Outcomes
Pair phone with HC-05
Send commands via Bluetooth
Decode commands on Arduino
Drive motors using TB6612

## Slide 4: Schematics
HC-05 TX→D10 (RX)
HC-05 RX→D11 (TX)
OLED SDA→A4, SCL→A5
TB6612 motor pins same as before

## Slide 5: Pseudocode – IR Receiver Logic
If BT has data:
Read command
F/B/L/R/S → motor actions
Optional speed: V150
Show command on OLED
GitHub: https://github.com/info-zas/zas-robotics-car-2-communications/tree/main/01_FoundationProjects/07_Bluetooth%20Control

## Slide 6: Command Protocol
F → Forward
B → Backward
L → Left
R → Right
S → Stop
V### → Speed

## Slide 7: Applications
Phone-controlled robots
Wireless manual override
Simple serial communication

## Slide 8: Q&A
Why SoftwareSerial?
Why iPhone can't pair HC-05?
How send joystick data?