## Slide 1: ZAS Robotic Products
Navigational Robotic Series
Robot Car-2: Communications
Lab Session 1 – Car Basic Movements

## Slide 2: Lab Session 1 – Car Basic Movements
Understand TB6612 motor control
Learn motor direction + speed pins
Build basic movement functions
Test movement on robot car

## Slide 3: Learning Outcomes
Explain direction + PWM control
Use digitalWrite + analogWrite
Move car: F / B / L / R / Stop
Debug wiring & logic

## Slide 4: Schematics
Left Motor: IN1=7, IN2=8, PWM=6
Right Motor: IN1=3, IN2=4, PWM=5
VM → Battery, GND shared, VCC→5V

## Slide 5: Pseudocode
Setup pins as OUTPUT
Functions: forward/backward/turn/stop
Loop: call movement functions

## Slide 6: Example Code
#define Left1 7
#define Left2 8
#define Left_Speed 6
#define Right1 3, Right2 4, Right_Speed 5
digitalWrite + analogWrite usage
GitHub Link:

## Slide 7: Applications
Foundation for wireless control
Used in delivery & warehouse robots
Supports future sensor integration

## Slide 8: Q&A
Why two motor pins?
What is PWM?
Why both LOW = motor off?