## Slide 1: ZAS Robotic Products
Navigational Robotic Series
Robot Car-2: Communications
Lab Session 2 – Joystick Movement Functionality

## Slide 2: Lab Session 2 – Joystick Movement Functionality
Read joystick on A0/A1
Determine direction
Display on OLED
Prepare for wireless control

## Slide 3: Learning Outcomes
Understand X/Y joystick values
Use analogRead for input
Apply dead-zone logic
Show direction on OLED

## Slide 4: Schematics
Joystick: VRx→A0, VRy→A1
GND→GND, VCC→5V
OLED: SDA→A4, SCL→A5

## Slide 5: Pseudocode
Read X & Y values
Determine direction
Clear OLED & print
Small delay

## Slide 6: Example Code
analogRead(A0/A1)
Direction thresholds
OLED text output
Dead zone logic
GitHub Link: https://github.com/info-zas/zas-robotics-car-2-communications/tree/main/01_FoundationProjects/02_Joystick_Movement_Functionality

## Slide 7: Direction Logic
Y>600 = Forward
Y<400 = Backward
X>600 = Right
X<400 = Left
Else = Center

## Slide 8: Applications
Robot steering
Variable speed control
Game controllers

## Slide 9: Q&A
Why dead zones?
How map tilt to speed?
What causes jitter?