## Slide 1: ZAS Robotic Products
Navigational Robotic Series
Robot Car-2: Communications
Lab Session 9 – Touch Control

## Slide 2: Lab Session 9 – Touch Control
Touch sensor on remote
NRF24 TX → RX
Car moves when touched
OLED feedback on both sides

## Slide 3: Learning Outcomes
Work with capacitive touch sensors
Transmit sensor state via RF24
Trigger robot movement
Debug using OLED

## Slide 4: Schematics
Touch → D4 on remote
NRF24 TX → RX same as before
OLED SDA→A4, SCL→A5
Car motors TB6612 pins unchanged

## Slide 5: Pseudocode – Remote Arduino
Read touch state HIGH/LOW
Create struct {touched}
Send via radio.write()
Show TOUCHED/NO TOUCH on OLED
GitHub: https://github.com/info-zas/zas-robotics-car-2-communications/tree/main/01_FoundationProjects/09_Touch_Sensor_Control

## Slide 6: Pseudocode – Car Arduino
radio.available() → read struct
If touched → Forward
Else → Stop
Show action on OLED
GitHub: https://github.com/info-zas/zas-robotics-car-2-communications/tree/main/01_FoundationProjects/09_Touch_Sensor_Control

## Slide 7: Command Protocol
TOUCHED → Move Forward
NO TOUCH → Stop Car

## Slide 8: Applications
Wireless start/stop
Remote-triggered robots
Simple IoT interactions

## Slide 9: Q&A
Why only send bool?
How add multiple sensors?
How avoid false triggers?