## Slide 1: Robot Car 2 (Wireless Communication Control) (RCC)
(Lesson Ref: RCC04)
RCC04:Robot Car Control Using Buttons

## Slide 2: Robot Car2 - Contents
Car 2 Transmitter Module (Front)
Car 2 Transmitter Module (Back)
Bluetooth Connector
Free Connector
Colour Sensor Connector
Gesture Sensor Connector
NRF 24L01
Transmitter
Joystick
Accelerometer
OLED
Mode
Button
Mini
Breadboard
Arduino
Uno
18650 Battery Holder
Button Control

## Slide 3: Robot Car2 - Contents
Car 2 Receiver Module (Front)
Car 2 Receiver Module (Back)
Car2 Receiver Motor Controller Board
NRF 24L01
Receiver
OLED
TB6612 Motor Driver
Battery Connector
18650 Battery Holder
Castor Wheel
DC Motors

## Slide 4: RCC04:Robot Car Control Using Buttons
Things Needed
Car 2 Receiver Module
Car 2 Transmitter Module

## Slide 5: RCC04:Robot Car Control Using Buttons
Code for Lesson RCC04 (RCC04_Robot_Car_Control_Using_Buttons_Tx.ino):
https://github.com/info-zas/zas-robotics-car-2-communications/blob/main/01_FoundationProjects/RCC04_Robot_Car_Control_Using_Buttons/RCC04_Robot_Car_Control_Using_Buttons_Tx/RCC04_Robot_Car_Control_Using_Buttons_Tx.ino
Code for Lesson RCC04 (RCC04_Robot_Car_Control_Using_Buttons_Rx.ino):
https://github.com/info-zas/zas-robotics-car-2-communications/blob/main/01_FoundationProjects/RCC04_Robot_Car_Control_Using_Buttons/RCC04_Robot_Car_Control_Using_Buttons_Rx/RCC04_Robot_Car_Control_Using_Buttons_Rx.ino

## Slide 6: RCC04:Robot Car Control Using Buttons
Note:
Ensure both the receiver/transmitter have the identical Device Address (Pipe) and Channel
Compact Code Summary
setup() • Start Serial (9600) • Init OLED (SSD1306, 0x3C) • Init nRF24L01 as TRANSMITTER (CE=A3, CSN=A2, addr "00001", ch 108, pwr LOW) • Configure buttons UP(7), DOWN(6), LEFT(5), RIGHT(4) using INPUT_PULLUP
loop() • Set default STOP (x = y = 512) • Read buttons (active LOW) and map to direction values – UP → FORWARD, DOWN → BACKWARD, LEFT → LEFT, RIGHT → RIGHT • Send {x, y} payload via radio • Display TRANSMITTER and direction on OLED • Delay 100 ms
Compact Code Summary
setup() • Start Serial (9600) • Init motor pins and set fixed speed (PWM = 150) • Init OLED (SSD1306, 0x3C) • Init nRF24L01 as RECEIVER (CE=A3, CSN=A2, pipe "00001", ch 108, pwr LOW)
loop() • Display CAR RECEIVER on OLED • If radio data available: – Read {x, y} payload – Decide motion using thresholds – Drive motors (FORWARD / BACKWARD / LEFT / RIGHT / STOP) • Refresh OLED, delay 100 ms
RCC04_Robot_Car_Control_Using_Buttons_Tx.ino
RCC04_Robot_Car_Control_Using_Buttons_Rx.ino