## Slide 1: Robot Car 2 (Wireless Communication Control) (RCC)
(Lesson Ref: RCC07)
RCC07:Robot Car Control Using IR

## Slide 2: Robot Car2 - Contents
Car 2 Transmitter Module (Front)
Car 2 Transmitter Module (Back)
Bluetooth Connector
Free Connector
Colour Sensor Connector
Gesture Sensor Connector
NRF 24L01
Transmitter
Joystick
Accelerometer
OLED
Mode
Button
Mini
Breadboard
Arduino
Uno
18650 Battery Holder
Button Control

## Slide 3: Robot Car2 - Contents
Car 2 Receiver Module (Front)
Car 2 Receiver Module (Back)
Car2 Receiver Motor Controller Board
NRF 24L01
Receiver
OLED
TB6612 Motor Driver
Battery Connector
18650 Battery Holder
Castor Wheel
DC Motors

## Slide 4: RCC07:Robot Car Control Using IR
Things Needed
Car 2 Receiver Module

## Slide 5: RCC07: IR Tx Codes
Code for Lesson RCC07 (RCC07_a_IR_Remore_Code_Rx.ino):
https://github.com/info-zas/zas-robotics-car-2-communications/blob/main/01_FoundationProjects/RCC07_Robot_Car_Control_Using_IR/RCC07_a_IR_Remore_Code_Rx/RCC07_a_IR_Remore_Code_Rx.ino
Each IR remote has its unique set of code for their keys.
First find the unique code for keys of your IR transmitter remote.
Upload the code (RCC07_a_IR_Remore_Code_Rx.ino ) and get the IR code for each key printed in the serial monitor.

## Slide 6: RCC07: IR Tx Codes

## Slide 7: RCC07:Robot Car Control Using IR
setup()
Init IR receiver on pin 12
Init motor control pins (Left & Right motors with PWM speed)
Set fixed motor speed using PWM (150)
Init OLED display (SSD1306, I2C, addr 0x3C)
Display startup message “IR READY” on OLED
Stop motors at startup
loop()
Wait for IR signal from remote
Decode received IR raw data
Match IR code to direction:
  FORWARD / BACKWARD / LEFT / RIGHT / STOP
Drive motors based on matched direction
Display current direction text on OLED
Resume IR receiver for next command
RC07_b_Robot_Car_Control_Using_IR_Rx.ino
Code for Lesson RCC07 (RCC07_b_Robot_Car_Control_Using_IR_Rx.ino):
https://github.com/info-zas/zas-robotics-car-2-communications/blob/main/01_FoundationProjects/RCC07_Robot_Car_Control_Using_IR/RCC07_b_Robot_Car_Control_Using_IR_Rx/RCC07_b_Robot_Car_Control_Using_IR_Rx.ino
Now that we have the code for the arrow keys of the remote, we can use them in the code to control the car movements.