## Slide 1: Robot Car 2 (Wireless Communication Control) (RCC)
(Lesson Ref: RCC08)
RCC08:Robot Car Control Using Bluetooth

## Slide 2: Robot Car2 - Contents
Car 2 Transmitter Module (Front)
Car 2 Transmitter Module (Back)
Bluetooth Connector
Free Connector
Colour Sensor Connector
Gesture Sensor Connector
NRF 24L01
Transmitter
Joystick
Accelerometer
OLED
Mode
Button
Mini
Breadboard
Arduino
Uno
18650 Battery Holder
Button Control

## Slide 3: Robot Car2 - Contents
Car 2 Receiver Module (Front)
Car 2 Receiver Module (Back)
Car2 Receiver Motor Controller Board
NRF 24L01
Receiver
OLED
TB6612 Motor Driver
Battery Connector
18650 Battery Holder
Castor Wheel
DC Motors

## Slide 4: RCC08:Robot Car Control Using Bluetooth
Things Needed
Car 2 Receiver Module

## Slide 5: RCC08: Bluetooth Module HC05
Code for RCC08_Robot_Car_Control_Using_Bluetooth_Rx.ino):
https://github.com/info-zas/zas-robotics-car-2-communications/blob/main/01_FoundationProjects/RCC08_Robot_Car_Control_Using_Bluetooth/RCC08_Roboti_Car_Control_Using_Bluetooth_Rx/RCC08_Roboti_Car_Control_Using_Bluetooth_Rx.ino
Install the App ‘Arduino Bluetooth Control’ from Play Store on your Android Smart Phone.
Remove the HC05 Bluetooth Module from the robot car
Upload the code RCC08_Robot_Car_Control_Using_Bluetooth_Rx.ino
Re-insert the HC05 Bluetooth Module in the car.

## Slide 6: RCC08: Bluetooth APP

## Slide 7: RCC08:Robot Car Control Using Bluetooth
setup()
Init Serial communication at 9600 baud (HC-05 default)
Configure motor control pins (IN1–IN4, ENA, ENB)
Stop motors at startup
loop()
Check for incoming Bluetooth data via Serial
Read single-character command from mobile app
Decode command and map to motion:
  F → Forward
  B → Backward
  L → Left
  R → Right
  S → Stop
Drive motors using direction pins and PWM speed control
RCC08_Robot_Car_Control_Using_Bluetooth_Rx.ino
Code for RCC08_Robot_Car_Control_Using_Bluetooth_Rx.ino):
https://github.com/info-zas/zas-robotics-car-2-communications/blob/main/01_FoundationProjects/RCC08_Robot_Car_Control_Using_Bluetooth/RCC08_Roboti_Car_Control_Using_Bluetooth_Rx/RCC08_Roboti_Car_Control_Using_Bluetooth_Rx.ino