## Slide 1: Robot Car 2 (Wireless Communication Control) (RCC)
(Lesson Ref: RCC11)
RCC11:Hybrid Robot Car Control Using IR-NRF

## Slide 2: Robot Car2 - Contents
Car 2 Transmitter Module (Front)
Car 2 Transmitter Module (Back)
Bluetooth Connector
Free Connector
Colour Sensor Connector
Gesture Sensor Connector
NRF 24L01
Transmitter
Joystick
Accelerometer
OLED
Mode
Button
Mini
Breadboard
Arduino
Uno
18650 Battery Holder
Button Control

## Slide 3: Robot Car2 - Contents
Car 2 Receiver Module (Front)
Car 2 Receiver Module (Back)
Car2 Receiver Motor Controller Board
NRF 24L01
Receiver
OLED
TB6612 Motor Driver
Battery Connector
18650 Battery Holder
Castor Wheel
DC Motors

## Slide 4: RCC11:Hybrid Robot Car Control Using IR-NRF
Things Needed
Car 2 Receiver Module
Car 2 Transmitter Module

## Slide 5: RCC11:Hybrid Robot Car Control Using IR-NRF
IR Remote
↓
IR Receiver (TX Arduino, pin 12)
↓
NRF24L01 (TX)
↓
NRF24L01 (RX)
↓
Motor Driver → Robot Car

## Slide 6: RCC11: IR Tx Codes
Code for Lesson RCC11 (RCC11_a_IR_Remore_Code_Tx.ino):
https://github.com/info-zas/zas-robotics-car-2-communications/blob/main/01_FoundationProjects/RCC11_Hybrid_Robot_Car_IR_NRF/RCC11_a_IR_Remore_Code_Tx/RCC11_a_IR_Remore_Code_Tx.ino
Each IR remote has its unique set of code for their keys.
First find the unique code for keys of your IR transmitter remote.
Upload the code (RCC11_a_IR_Remore_Code_Tx.ino ) and get the IR code for each key printed in the serial monitor.

## Slide 7: RCC11: IR Tx Codes

## Slide 8: RCC11:Hybrid Robot Car Control Using IR-NRF
setup()
Init IR receiver on pin 12
Init NRF24L01 as TRANSMITTER
  CE = A3, CSN = A2
  Address = "00001", Channel = 108
  PA Level = LOW, TX mode enabled
Start Serial for debugging
loop()
Wait for IR remote input
Decode IR raw data
Map IR codes to commands:
  0xE718FF00 → F (Forward)
  0xAD52FF00 → B (Backward)
  0xF708FF00 → L (Left)
  0xA55AFF00 → R (Right)
  0xE31CFF00 → S (Stop)
Send 1-byte command via NRF24L01
Resume IR receiver for next input
RCC11_b_Hybrid_Robot_Car_IR_NRF_Tx.ino
Code for Lesson RCC11 (RCC11_b_Hybrid_Robot_Car_IR_NRF_Tx.ino)
https://github.com/info-zas/zas-robotics-car-2-communications/blob/main/01_FoundationProjects/RCC11_Hybrid_Robot_Car_IR_NRF/RCC11_b_Hybrid_Robot_Car_IR_NRF_Tx/RCC11_b_Hybrid_Robot_Car_IR_NRF_Tx.ino
Now that we have the code for the arrow keys of the remote, we can use them in the code the transmitter.

## Slide 9: RCC11:Hybrid Robot Car Control Using IR-NRF
Upload the receiver code
RCC11_b_Hybrid_Robot_Car_IR_NRF_Rx.ino in the robot car.
Code for RCC11_b_Hybrid_Robot_Car_IR_NRF_Rx.ino):
https://github.com/info-zas/zas-robotics-car-2-communications/blob/main/01_FoundationProjects/RCC11_Hybrid_Robot_Car_IR_NRF/RCC11_b_Hybrid_Robot_Car_IR_NRF_Rx/RCC11_b_Hybrid_Robot_Car_IR_NRF_Rx.ino

## Slide 10: RCC11:Hybrid Robot Car Control Using IR-NRF
setup()
Configure motor driver pins (IN1–IN4, ENA, ENB)
Stop motors at startup
Init NRF24L01 as RECEIVER
  CE = A3, CSN = A2
  Address = "00001", Channel = 108
  PA Level = LOW, Listening mode enabled
Start Serial for debugging
loop()
Check for incoming NRF24L01 data
Read 1-byte command from transmitter
Decode command and map to motor action:
  F → Forward
  B → Backward
  L → Left
  R → Right
  S / other → Stop
Drive motors using direction pins and PWM speed control
RCC11_b_Hybrid_Robot_Car_IR_NRF_Rx.ino